## Slide 1: CHAPTER 10: ELECTROMAGNETISM
Master Classroom Lecture & Concept Deck
Vardaan Learning Institute

## Slide 2: 1. Oersted's Historic Experiment (1820)
Electric current produces a surrounding magnetic field.
SNOW Rule: Current South to North Over needle -> North pole deflects West.
Reversing current reverses magnetic deflection direction.

## Slide 3: 2. Properties of Magnetic Field Lines
Continuous closed loops from North to South outside magnet.
Tangent at any point gives the magnetic field direction.
Two field lines NEVER intersect (avoids two directions at one point).
Neutral Points: Resultant field is zero where wire field cancels Earth's BH.

## Slide 4: 3. Straight Conductor & Thumb Rule
Concentric circular field lines in planes perpendicular to the wire.
Field strength B is proportional to Current (I) and inversely to distance (r).
Right-Hand Thumb Rule: Thumb along current -> curled fingers give field direction.

## Slide 5: 4. Circular Loop & Clock Face Rule
Concentric circular lines near wire segments; straight and uniform at the center.
Clock Face Rule: Clockwise current = South Pole (S) | Anticlockwise = North Pole (N).
Central field strength B is proportional to N * I / (2 * r).

## Slide 6: 5. Magnetic Field in a Solenoid
Helical coil carrying current behaves exactly like a permanent bar magnet.
Interior field lines are straight, parallel, and densely packed (Uniform Field).
Strength factors: turns per unit length (n), current (I), soft iron core.

## Slide 7: 6. Electromagnets vs Permanent Magnets
Electromagnet: Temporary magnet on a high-permeability soft iron core.
Soft iron loses magnetism instantly (low retentivity/coercivity); steel retains it.
U-shaped core brings poles together for high magnetic flux concentration.

## Slide 8: 7. The Electric Bell Assembly & Cycle
Components: U-shaped electromagnet, soft iron armature, flat spring, hammer, gong, contact screw.
Working: Current magnetizes core -> attracts armature -> hammer strikes gong -> breaks contact -> repeats.

## Slide 9: 8. Force on Conductor (Lorentz Force)
Lorentz Force: F = I * L * B * sin(theta). Maximum at 90 deg; zero parallel to field.
Kicking Wire Experiment demonstrates mechanical force on conductor in magnetic field.

## Slide 10: 9. Fleming's Left-Hand Rule & DC Motor
Left-Hand Rule: Thumb = Motion (F), Forefinger = Field (B), Middle Finger = Current (I).
DC Motor converts Electrical Energy into Mechanical (Rotational) Energy.
Split-Ring Commutator reverses current every 180 degrees to maintain unidirectional rotation.

## Slide 11: 10. Faraday's Laws of Induction
Electromagnetic Induction: Induced EMF produced when magnetic flux changes with time.
Faraday's Law: e = -N * (delta Phi / delta t).
Lenz's Law: Induced current opposes the cause producing it (Conservation of Energy).

## Slide 12: 11. AC Generator (Alternator) & AC Wave
AC Generator converts Mechanical Energy into Alternating Current.
Continuous Slip Rings (R1, R2) output sinusoidal AC.
Indian Household Supply: 220 V RMS, 50 Hz frequency, 100 reversals per second.

## Slide 13: 12. Transformers (Step-Up & Step-Down)
Principle: Mutual Induction between Primary (P) and Secondary (S) coils.
Step-Up: Vs > Vp, Ns > Np, Is < Ip (thick primary wire, thin secondary wire).
Step-Down: Vs < Vp, Ns < Np, Is > Ip (thin primary wire, thick secondary wire).
Laminated silicon steel core prevents eddy current heat losses.

## Slide 14: 13. Quick Revision Formula Matrix
Transformation Ratio: Vs / Vp = Ns / Np = Ip / Is = n
Power: Pin = Vp * Ip, Pout = Vs * Is | Efficiency: (Pout / Pin) * 100%
Motor = Left-Hand Rule | Generator = Right-Hand Rule | Transformer = Mutual Induction